XGPC-P9T2R-CD2C

# SFP+ COMBO PON OLT D2/C+ Transceiver

Features

- Compatible with GPON &XGPON system. Work in GPON & XGPON system simultaneously.

- XGPON: Single fiber bi-directional data links TX 9.95Gbps, RX 2.488Gbps application. GPON: Single fiber bi-directional data links asymmetric TX 2488Mbps/RX1244Mbps application

- 0 to 70°C operating case temperature

- 3.3V power supply

- SFP+ package with SC Receptacle connector

- Hot-pluggable capability

- XGPON: High power 1577nm EML LD & High sensitivity 1270nm APD. GPON: 1490nm DFB LD & High sensitivity 1310nm APD

- Support 20km transmission distance with SMF

- SD indication for GPON&XGPON

- Low EMI and excellent ESD protection

- Digital diagnostic monitor interface

- RoHS6 compliance

Applications

- GPON OLT CLASS C+ & XGPON D2 SFP+ OLT

STANDARDS

- Complies with SFF-8472

- Complies with ITU G.987.2

- Complies with ITU-T G.984.2

- Complies with FCC 47 CFR Part 15, Class B

- Complies with FDA 21 CFR 1040.10 and 1040.11

Absolute Maximum Ratings

Table 1- Absolute Maximum Ratings

| Parameter | Symbol | Min | Max | Units | Notes |
| --- | --- | --- | --- | --- | --- |
| Storage Ambient Temperature | TSTG | -40 | 85 | °C |  |
| Operating Case Temperature | TA | 0 | 70 | °C |  |
| Operating Humidity | OH | 5 | 85 | % |  |
| VCC3 Power Supply Voltage | VCC3 | 0 | 3.6 | V |  |

Recommended Operating Environment

Table 2 - Recommended Operating Environment

| Parameter | Symbol | Min | Typical | Max | Units | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Operating Case Temperature | Tc | 0 |  | +70 | °C |  |
| VCC3 Power Supply Voltage | Vcc | 3.13 | 3.3 | 3.47 | V |  |
| Date Rate | XGPON GPON |  | 9.953/2.488 2.488/1.244 |  | Gbps Gbps |  |
| Power Consumption | P |  | - | 3.3 | W |  |

XGPON Optical Characteristics

Table 3- XGPON Optical Characteristics

| Transmitter |
| --- |
| Parameter | Symbol | Min. | Typical | Max. | Unit | Notes |
| Optical Center Wavelength | λC | 1575 |  | 1580 | nm |  |
| Optical Spectrum Width (-20dB) | ∆λ | - | - | 1 | nm |  |
| Side Mode Suppression Ratio | SMSR | 30 |  |  | dB |  |
| Optical Waveform Diagram | Compliant with ITU G.987.2 | Figure 1 |
| Average Launch Optical Power | AOP | +5.5 |  | +8 | dBm | Launched into SMF @ 25℃ |
| Average Launch Optical Power | AOP | +5 |  | +8 | dBm | Launched into SMF @ 0~70℃ |
| Power-OFF Transmitter Optical Power |  |  |  | -39 | dBm | Launched into SMF@0~70℃ |
| Extinction Ratio | ER | 8.2 |  |  | dB | PRBS231-1 @9.95Gbps |
| Receiver |
| Operating Wavelength |  | 1260 |  | 1280 | nm |  |
| Max Optical input |  |  |  | -3 | dBm | input without incurring damage |
| Sensitivity(BOL) | SEN |  |  | -30.5 | dBm | PRBS 223-1@2.488Gbps BER ≤1×10-4 |
| Sensitivity(EOL) | SEN |  |  | -29.5 | dBm | PRBS 223-1@2.488Gbps BER ≤1×10-4 |
| Saturation Optical Power | SAT | -9 |  |  | dBm | PRBS 223-1@2.488Gbps BER ≤1×10-4 |
| SD Assert Level(BOL) |  |  |  | -31 | dBm | =SEM-0.5dB |
| SD Assert Level(EOL) |  |  |  | -30 | dBm | =SEN-0.5dB |
| SD De-assert Level |  | -43 |  |  | dBm |  |
| Hysteresis |  | 0.5 |  | 6 | dB |  |
| Receiver Reflectance |  |  |  | -20 | dB |  |

GPON Optical Characteristics

Table 4- GPON Optical Characteristics

| Transmitter |
| --- |
| Parameter | Symbol | Min. | Typical | Max. | Unit | Notes |
| Optical Center Wavelength | λC | 1480 |  | 1500 | nm |  |
| Optical Spectrum Width (-20dB) | ∆λ |  |  | 1 | nm |  |
| Side Mode Suppression Ratio | SMSR | 30 |  |  | dB |  |
| Optical Waveform Diagram | ITU-T G.984.2 | Figure 2 |
| Average Launch Optical Power | AOP | +4 |  | +7 | dBm | Launched into SMF @ 25℃ |
| Average Launch Optical Power | AOP | +3 |  | +7 | dBm | Launched into SMF @ 0~70℃ |
| Power-OFF Transmitter Optical Power |  |  |  | -39 | dBm | Launched into SMF @ 0~70℃ |
| Extinction Ratio | ER | 8.2 |  |  | dB | PRBS 223-1+72CID @2.488Gbps |
| Receiver |
| Operating Wavelength |  | 1290 |  | 1330 | nm |  |
| Max Optical input |  |  |  | -3 | dBm | input without incurring damage |
| Sensitivity (BOL) | SEN |  |  | -31 | dBm | PRBS 223-1@1.244Gbps BER ≤1×10-10 |
| Sensitivity (EOL) | SEN |  |  | -30 | dBm | PRBS 223-1@1.244Gbps BER ≤1×10-10 |
| Saturation Optical Power | SAT | -12 |  |  | dBm | PRBS 223-1@1.244Gbps BER ≤1×10-10 |
| SD Assert Level(BOL) |  |  |  | -31.5 | dBm | =SEN-0.5dB |
| SD A ssert Level(EOL) |  |  |  | -30.5 |  | =SEN-0.5dB |
| SD De-assert Level |  | -43 |  |  | dBm |  |
| Hysteresis |  | 0.5 |  | 8 | dB |  |
| Receiver Reflectance |  |  |  | -20 | dB |  |

XGPON Transmitter Electrical Characteristics

Table 5- XGPON Transmitter Electrical Characteristics

| Parameter | Symbol | Min. | Typical | Max. | Unit | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Data Input Differential Swing |  | 120 |  | 850 | mV | CML input, AC coupled |
| Input Differential Impedance |  | 90 | 100 | 110 | Ω |  |
| Transmitter Enable Voltage - Low |  | 0 |  | 0.8 | V |  |
| Transmitter Disable Voltage - High |  | 2.0 |  | VCC | V |  |

GPON Transmitter Electrical Characteristics

Table 6- GPON Transmitter Electrical Characteristics

| Parameter | Symbol | Min. | Typical | Max. | Unit | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Data Input Differential Swing |  | 200 |  | 1600 | mV | LVPECL input, AC coupled |
| Input Differential Impedance |  | 90 | 100 | 110 | Ω |  |
| Transmitter Disable Voltage - Low |  | 0 |  | 0.8 | V |  |
| Transmitter Disable Voltage - High |  | 2.0 |  | VCC | V |  |
| Transmitter Fault Alarm Voltage - Low |  | 0 |  | 0.4 | V |  |
| Transmitter Fault Alarm Voltage – High |  | 2.4 |  | Vcc | V |  |

XGS PON Transmitter Eye Mask Definitions And Test Procedure

Figure 1 XGPON Transmitter Eye Mask Definitions

| X3-X2 | Y1 | Y2 | Y3 | Y4 | Unit |
| --- | --- | --- | --- | --- | --- |
| 0.2 | 0.25 | 0.75 | 0.25 | 0.25 | UI |

GPON TRANSMITTER EYE MASK DEFINITIONS AND TEST PROCEDURE

Figure 2 GPON Transmitter Eye Mask Definitions

RECEIVER ELECTRICAL CHARACTERISTICS

Table 7- RECEIVER ELECTRICAL CHARACTERISTICS

| Parameter | Symbol | Min. | Typical | Max. | Unit | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Data Output Differential Swing(XGPON) |  | 340 |  | 850 | mV | CML output, DC coupled |
| Data Output Differential Swing(GPON) |  | 400 |  | 1600 | mV | LVPECL output, DC coupled |
| Reset width(XGPON) | Trw | 25.6 |  |  | ns | Figure 3 |
| Reset width(GPON) | Trw | 12.8 |  |  | ns | Figure 3 |
| Signal Detect Assert Time | Tsda1 |  |  | 50 | ns | Figure 3 |
| Signal Detect Assert Time | Tsda2 |  |  | 50 | ns | Figure 3 |
| Signal Detect De-assert Time | Tsdd |  |  | 12.8 | ns | Figure 3 |
| Data recovery time | Trec |  |  | 50 | ns | Figure 3 |
| Reset To ONU Optical Time | Trto | 0 | - | 250 | us | Figure 3 |
| Reset Guard Time | Trg | 0 | - | 250 | us | Figure 3 |
| Reset-Low |  | 0 |  | 0.8 | V |  |
| Reset-High |  | 2.0 |  | VCC | V |  |
| Signal Detect Voltage-Low |  | 0 |  | 0.4 | V |  |
| Signal Detect Voltage-High |  | 2.4 |  | VCC | V |  |
| RSSI Trigger-Low |  | 0 |  | 0.8 | V |  |
| RSSI Trigger-High |  | 2.0 |  | VCC | V |  |
| Upstream Signal Width | TONT | 300 |  |  | ns | Figure 5 |
| RSSI Trigger Delay | TD | 0 |  | 3000 | ns | Figure 5 |
| RSSI Trigger Width | TW | 300 |  |  | ns | Figure 5 |
| I2C Access Prohibited Time | TP | 500 |  |  | us |  |

Timing Parameter Definitions In Burst Mode Sequence

Figure 3 Timing Parameter Definitions in Burst Mode Sequence

BURST MODE RECEIVER DYNAMIC RANGE

Strong Signal From ONU

Figure 4 Burst Mode Receiver Dynamic Range

TIMING PARAMETER DEFINITIOINS IN RSSI TRIGGER

Figure 5 Timing Parameter Definitions in RSSI Trigger

PIN OUT DRAWING

Figure 6 Pin Out Drawing

PIN DESCRIPTION

Table 8- PIN OUT DRAWING

| PIN | Name | Description | Notes |
| --- | --- | --- | --- |
| 1 | GPON_TX+ | GPON Non-Inverted Transmit Data in | LVPECL input, AC coupled |
| 2 | GPON_TX- | GPON Inverted Transmit Data in | LVPECL input, AC coupled |
| 3 | GND | Module Ground |  |
| 4 | SDA | The data line | The data line of two wire serial interface |
| 5 | SCL | The clock line | The clock line of two wire serial interface |
| 6 | GPON_RD- | GPON Non-inverted Received Data Out | LVPECL output, DC coupled; No squelch function |
| 7 | XGPON_RST | XGPON Burst Receiver Reset | LVTTL, High level Reset |
| 8 | XGPON_SD | XGPON SD Indication | LVTTL output, active LOW when the receiver lost signal |
| 9 | TX_DIS/Trig | Transmitter Disable | LVTTL Input by 10k pull up resistor, Low: transmitter on |
| 10 | GPON_RD+ | GPON Non-inverted Received Data Out | LVPECL output, DC coupled; No squelch function |
| 11 | GND | Module Ground |  |
| 12 | XGPON_RD- | XGPON Inverted Received Data Out | CML output, DC coupled; No squelch function |
| 13 | XGPON_RD+ | XGPON Non-inverted Received Data Out | CML output, DC coupled; No squelch function |
| 14 | GPON_SD | GPON SD Indication | LVTTL output, active LOW when the receiver lost signal |
| 15 | VCC3_RX | Receiver 3.3V Power Supply |  |
| 16 | VCC3_TX | Transmitter 3.3V Power Supply |  |
| 17 | GPON_RST | GPON Burst Receiver Reset | LVTTL, High level Reset |
| 18 | XGPON_TX+ | XGPON Non-Inverted Transmit Data in | CML input, AC coupled |
| 19 | XGPON_TX- | XGPON Inverted Transmit Data in | CML input, AC coupled |
| 20 | GND | Module Ground |  |

TYPICAL INTERFACE CIRCUIT

Figure 7 Typical Interface Circuit

PACKAGE OUTLINE

Figure 8 Package Outline

EEPROM INFORMATION

Figure 9 EEPROM Memory Map Specific Data Field Descriptions

Digital Diagnostic Monitoring Interface

Table 9- Digital Diagnostic Monitoring Interface

| Parameter | Range | Accuracy | Calibration | Notes |
| --- | --- | --- | --- | --- |
| Temperature | -5 to 75°C | ±3°C | Internal | LSB: 1/256C |
| Voltage | 3.0 to 3.6V | ±5% | Internal | LSB: 0.1mV |
| Bias Current | 0 to 262mA | ±10% | Internal | LSB: 4uA |
| TX Power | XGPON:2 to 10dBm GPON:1 to 9dBm | ±3dB | Internal | LSB: 0.2uW |
| RX Power | XGPON:-30 to -9dBm GPON:-31 to -12dBm | ±3dB | Internal | LSB: 0.1uW |

Order Information

Table 10- Ordering information

| PN | Temperature Rating | Unit |
| --- | --- | --- |
| XGPC-P9T2R-CD2C | 0 ~ 70 | ℃ |

# Text boxes

Average Power Level of the Strong Signal

>15dB Dynamic Range

Weak Signal From ONU

Average Power Level of the weak Signal

Vee T

22 uF

HOST VCC3

0.1 uF

V  T

0. 1 uF

4.7~10K Ω

2X4.7 uH

22uF

0.1 uF

cc

Vcc R

Vee R RX_SD

Ser Data In+

Z= 50 Ω

Z= 50 Ω

RD+

RD-

Ser Data In-

Limiting

RX_Reset

Amplifier

SerDes

Host Board

Ser Data Out+

TD+

Ser Data Out -

Z= 50 Ω

Z= 50 Ω

TD+

Laser

Driver

TX_DIS

HOST VCC

4.7-10k

SDA

SCL

Vcc T

MCU

RSSI-Trig

Temperature Bias Current Supply Voltage Output Power Received Power

4.7～10kΩ