## Slide 1
OTU4/OTUC2
Function and Feature | Description (Line Mode)
ALS | Supported on the client side
Tunable wavelength | Supports tunable wavelengths in the range of 96 wavelengths with 50 GHz spacing in the extended C band.
PRBS | Supported
ESC | Supported
LPT | Supported
Error correction coding | Client side: RS-FEC (100GE access) WDM side: SDFEC2 (100G_QPSK, 100G_DQPSK, or 200G_e16QAM) SDFEC (200G_16QAM or 200G_16QAM-H)
Latency measurement | Supported
MAC Test frame | Supported when the client-side service type is GE/10GE LAN/25GE/40GE/100GE.
Protection scheme | Optical line 1+1/Extended intra-board 1+1/Client 1+1 protection
Loopback | Supported
Service encryption | Supported
MD02
A
MUX/DMUX
Client device
Service
Function
Line mode
OTU4/OTUC2
MD02
A
MUX
DMUX
OTU4/OTUC2
Regeneration mode
GE/10GE/25GE/40GE/100GE/FC100/FC200CFC400FC800/
FC1200/FC1600/3200/OTU2/
STM-64/OTU2E/OTU4/10GWAN
Board | Weight | Typical Power Consumption | Maximum Power Consumption
MD02A | 2.5 kg | 214 W | 242 W
Mechanical Specifications
MD02A is a dual-channel 100G/200G programmable optical transponder unit (OTU) board that implements conversion between Any 8G to 100G services and OTU4/OTUC2 signals.
MD02A
Start version: V100R019C10
Width:5U

## Slide 2
Client Side
QSFP-DD-100G(10x10G)-1310nm(LR10)-MPO-SMF-10km
QSFP28-100G(4x25G)-850nm(SR4)-MPO-MMF-0.1km
QSFP28-100G(4x25G/28G,Dualrate)-1295nm～1310nm(LR4)-SMF-10km
QSFP28-100G(4x25G)-1271～1331nm(CLR4)-SMF-2km NOTE：When the DC908 uses this optical module, it supports only CWDM4 but not CLR4 specifications.
QSFP+ -40G(4x10G)-850nm(SR4)-MPO-MMF-0.3km
QSFP+ -40G(4x10G)-1310nm(PSM4)-MPO-SMF-10km
QSFP+ -40G(4x10G)-1271nm～1331nm(CWDM,LR4)-SMF-10km
SFP+ -8.5G～10.5G-850nm-MMF-0.3km
SFP+ -10G(with CDR)-1310nm-SMF-10km
SFP+ -GE(LX)/10GE(LR/LW)-1310nm-SMF-10km
SFP+ -10G(10GE,LR/LW)-1310nm-SMF-10km
SFP+ -10G(with CDR)-1550nm-SMF-40km
SFP+ -10G-1550nm-SMF-40km
SFP+ -10G(10GE,ZR/ZW)-1550nm-SMF-80km
Optical Module
MD02A is a dual-channel 100G/200G programmable optical transponder unit (OTU) board that implements conversion between Any 8G to 100G services and OTU4/OTUC2 signals.
MD02A
Start version: V100R019C10
Width:5U
Client Side
SFP+ -10G(with CDR)-1550nm-SMF-80km
SFP+ -14G-850nm-MMF-0.1km
SFP28-28.05G-1310nm-SMF-10km
SFP28-28.05G-850nm-MMF-0.1km
SFP28-25G-850nm-LC-MMF-0.1km
SFP28-25G-1310nm-10km-SM-I
eSFP-1.25G-1310nm-SMF-10km
eSFP-4.25G-1310nm-SMF-10km Specifications
eSFP-4.25G-850nm-MMF-0.3km Specifications
eSFP,850nm,2.125Gb/s(Multi rate) ,-9.5 to -2.5dBm,-17dBm,LC,MM,0.5km
eSFP,1310nm,1.25Gb/s,-9 to -3dBm,-20dBm,LC,Single Mode,10km
eSFP,1310nm,1.25Gb/s,-5 to 0dBm,-23dBm,LC,SM,40km
eSFP,1550nm,1.25Gb/s,-2 to 5dBm,-23dBm,LC,SM,80km-01
eSFP,Tx1490nm/Rx1310nm,1.25Gb/s,-9dBm,-3dBm,-19.5dBm,LC,SM,10km

## Slide 3
Client Side
eSFP,Tx1310nm/Rx1490nm,1.25Gb/s,-9dBm,-3dBm,-19.5dBm,LC,SM,10km
eSFP,1310nm(Tx)/1480~1580nm(Rx),125M~1.25Gb/s,-2dBm,3dBm,-21dBm,LC,SM,40km
eSFP,1490nm(Tx)/1310nm(Rx),1.25Gb/s,-2dBm,3dBm,-23dBm,LC,SM,40km
WDM Side
Extended C band-Tunable wavelength-ePDM-200G e16QAM/100G QPSK/etc.(SDFEC2, 80km, A29)-CFP2
Extended C band-Tunable wavelength-200G e16QAM/100G QPSK/etc.(Short Distance, High Optical Power, T27)-Unpluggable
Extended C band-Tunable wavelength-200G e16QAM/100G QPSK/etc.(80km, High Optical Power, T29)-Unpluggable
Super C band-Tunable wavelength-200G e16QAM/100G QPSK/etc.(SDFEC2, 80km, U29)-Unpluggable
200G CFP2A29(80km,SDFEC2@200G e16QAM/100G QPSK/etc.,flex rate, Coherent,Tunable,Super C,-10dBm-4dBm,-18dBm,Flexgrid),high power
Optical Module
MD02A is a dual-channel 100G/200G programmable optical transponder unit (OTU) board that implements conversion between Any 8G to 100G services and OTU4/OTUC2 signals.
MD02A
Start version: V100R019C10
Width:5U